## Slide 1
Welding a Qualification Test

## Slide 2: Performing the Weld
The welder is set
The test plates are ready
Practice welds are complete, and you are ready to weld
Now what?

## Slide 3: Performing the Weld
Heat Control!
Clamp your weld plates so that they stay flat while welding
The heat from the weld will cause the weld plates to distort
Clamping the plates will minimize distortion
Keep the weld plates clamped until the weld is cool

## Slide 4: Performing the Weld
Preheat Temperature
If preheating is required, the preheat temperature will be indicated on the WPS
Preheat your test plates to the required preheat temperature
Check the temperature of the metal by using a temperature indicating crayon, or other means to measure temperature

## Slide 5: Performing the Weld
Interpass temperature
An interpass temperature will be indicated on the WPS
Check the temperature between every weld pass
Ensure that the temperature of the base metal does not exceed the interpass temperature
If the base metal temperature is higher than the interpass temperature on the WPS, then wait and allow the metal to cool below the interpass temperature before making the next pass
Never quench or attempt to accelerate cooling during a welding test

## Slide 6: Performing the Weld
Between Passes:
Chip slag, if necessary
Wire-brush weld passes
Check the temperature of the base metal
Inspect your weld for discontinuities or defects; make sure your weld is completely clean before making the next pass
Depending on the test and the test conductor, you may or may not be allowed to use power tools, such as grinders, during the test
If qualifying with a flux process (SMAW, FCAW), be especially vigilant when inspecting for slag inclusions, and remove all slag before the next pass

## Slide 7: Performing the Weld
When the weld is completed, let it cool slowly on its own
Never quench or accelerate cooling of a weld test at any point
Once the weld is completely cooled, remove the clamps

## Slide 8
www.realityworks.com